## Slide 1
Smart Parking and
EV Charger Monitoring
Fog and Serverless Cloud Architecture on AWS
Harish Ramasamy
MSc Cloud Computing · National College of Ireland · 2026
Module: Fog and Edge Computing · Lecturer: Giovani Estrada · Student ID: 24194654
5 IoT Sensors
AWS Serverless Backend
GitHub Actions CI/CD

## Slide 2
Abstract & System Architecture
Smart Parking and EV Charger Monitoring · Harish Ramasamy · MSc Cloud Computing, NCI · 2026
Abstract
A Smart Parking and EV Charger Monitoring System built on fog computing and serverless AWS cloud architecture. Five virtual sensor simulators feed a Python fog node that filters, deduplicates, and enriches data before dispatching to Amazon SQS → AWS Lambda → DynamoDB → API Gateway. A React.js dashboard provides real-time visualisation. Deployment is fully automated via GitHub Actions CI/CD to Amazon EC2.
5
IoT Sensors
4
AWS Services
7
Figures
3-Layer Architecture
LAYER 1 — SENSOR
Parking
EV Charger
Temperature
Air Quality
Vehicle Counter
↓
LAYER 2 — FOG NODE
Validate
Deduplicate
Alert
Enrich
Forward
↓
LAYER 3 — AWS CLOUD
API GW
SQS
Lambda
DynamoDB
Dashboard

## Slide 3
Sensor Layer & Fog Node
Smart Parking and EV Charger Monitoring · Harish Ramasamy · MSc Cloud Computing, NCI · 2026
Sensor
Key Data Fields
Rate
Alert Condition
Parking Occupancy
occupied, available, pct_full
5 s
> 90% full
EV Charger
status, power_kw, session_min
10 s
FAULT status
Temperature
temp_c, humidity_pct
8 s
> 45°C
Air Quality
co2_ppm, pm25, aqi_score
15 s
AQI > 150
Vehicle Counter
entries, exits, net_flow
3 s
flow > 10
Fog Node — 6-Step Pipeline
1. Receive payload via HTTP POST
2. Validate fields & data types
3. Deduplicate via in-memory timestamp cache
4. Apply threshold rules → alert flags
5. Enrich with fog ID & timestamp
6. Forward to API Gateway (3× retry)
fog_node.py — /ingest endpoint
@app.route('/ingest', methods=['POST'])
def ingest():
data = request.get_json()
if is_duplicate(data):
return 'dropped', 200
alert = check_threshold(data)
enriched = enrich(data, alert)
forward_to_cloud(enriched)
return jsonify({'status':'ok'})

## Slide 4
AWS Cloud Backend & Real-Time Dashboard
Smart Parking and EV Charger Monitoring · Harish Ramasamy · MSc Cloud Computing, NCI · 2026
API Gateway
REST /data
→
Amazon SQS
Message Queue
→
AWS Lambda
Event Processor
→
DynamoDB
NoSQL Store
→
EC2 Host
React Dashboard
Scalability Highlights
API Gateway:
Auto-scales — no server management
Amazon SQS:
Buffers traffic spikes, decouples layers
AWS Lambda:
1000× concurrent auto-scale on demand
DynamoDB:
On-demand RCU/WCU — no manual sizing
CI/CD Pipeline:
11 successful runs, avg deploy < 40 s
React.js Dashboard
▸ Live metric updates for all 5 sensor types
▸ Colour-coded 50-bay parking grid
▸ EV charger cards — status, kW, vehicle ID
▸ Live Power Draw bar chart (8 chargers)
▸ Occupancy trend line chart
▸ Environmental panel — temp, humidity, lux
▸ Real-time alerts feed for anomaly events

## Slide 5
CI/CD Pipeline & Results
Smart Parking and EV Charger Monitoring · Harish Ramasamy · MSc Cloud Computing, NCI · 2026
GitHub Actions CI/CD Pipeline
1
Code Push
git push to main triggers workflow
2
Install
pip install -r requirements.txt
3
Test
pytest tests/ — automated unit tests
4
Deploy
SSH to EC2, git pull, restart services
5
Health Check
curl /health — verify endpoint live
github.com/Harish-816/smart-parking-ev
11 successful runs · avg deployment < 40 seconds
Results & Discussion
✓ Fog reduces cloud load
Local filtering eliminates redundant upstream data, reducing cloud processing overhead.
✓ Scalable AWS pipeline
SQS-Lambda absorbs traffic spikes. DynamoDB on-demand capacity handles varying workloads.
✓ React.js dashboard
Real-time insights on parking, chargers, power, environment and active alerts — auto-refreshing.
✓ CI/CD validated
11 automated runs confirmed. Average EC2 deployment time consistently under 40 seconds.

## Slide 6
Conclusion & Thank You
This project demonstrates a 3-layer fog and edge computing architecture for smart city IoT monitoring. By filtering, deduplicating, and enriching data at the fog layer before cloud transmission, the system achieves reduced latency, lower bandwidth usage, and elastic scalability. The serverless AWS backend and automated CI/CD pipeline make it production-ready.
5 IoT Sensors
Parking · EV · Temp
Air Quality · Vehicle
Serverless AWS
API GW→SQS
→Lambda→DynamoDB
CI/CD Automated
GitHub Actions
11 successful runs
github.com/Harish-816/smart-parking-ev
Harish Ramasamy · x24194654@student.ncirl.ie · Thank You!